## Slide 1
Initial Results from the
Mars Science Laboratory
Your Name Here
MSL Science Team
9/27/12
NASA/JPL-Caltech/MSSS

## Slide 2
Curiosity’s Science Objectives
NASA/JPL-Caltech
Curiosity’s primary scientific goal is to explore and quantitatively assess a local region on Mars’ surface as a potential habitat for life, past or present
Biological potential
Geology and geochemistry
Role of water
Surface radiation

## Slide 3
Curiosity’s Science Payload
REMOTE SENSING
Mastcam (M. Malin, MSSS) - Color and telephoto imaging, video, atmospheric opacity
ChemCam (R. Wiens, LANL/CNES) – Chemical composition; remote micro-imaging
CONTACT INSTRUMENTS (ARM)
MAHLI (K. Edgett, MSSS) – Hand-lens color imaging
APXS (R. Gellert, U. Guelph, Canada) - Chemical composition
ANALYTICAL LABORATORY (ROVER BODY)
SAM (P. Mahaffy, GSFC/CNES/JPL-Caltech) - Chemical and isotopic composition, including organics
CheMin (D. Blake, ARC) - Mineralogy
ENVIRONMENTAL CHARACTERIZATION
MARDI (M. Malin, MSSS) - Descent imaging
REMS (J. Gómez-Elvira, CAB, Spain) - Meteorology / UV
RAD (D. Hassler, SwRI) - High-energy radiation
DAN (I. Mitrofanov, IKI, Russia) - Subsurface hydrogen
Wheel Base: 2.8 m
Height of Deck: 1.1 m
Ground Clearance: 0.66 m
Height of Mast: 2.2 m
Mass: 900 kg
DAN
REMS
ChemCam
Mastcam
RAD
MAHLI
APXS
Brush
Drill / Sieves
Scoop
MARDI

## Slide 4
Target: Gale Crater and Mount Sharp
NASA/JPL-Caltech/ESA/DLR/FU Berlin/MSSS
NASA/JPL-Caltech

## Slide 5
NASA/JPL-Caltech/ESA/DLR/FU Berlin/MSSS
150-km Gale Crater contains a 5-km high mound of stratified rock. Strata in the lower section of the mound vary in mineralogy and texture, suggesting that they may have recorded environmental changes over time. Curiosity will investigate this record for clues about habitability, and the ability of Mars to preserve evidence about habitability or life.
Target: Gale Crater and Mount Sharp
NASA/JPL-Caltech
?

## Slide 6
Landing precision for Curiosity
and previous Mars surface missions
NASA/JPL-Caltech/ESA

## Slide 7
Curiosity on parachute, imaged by
HiRISE on the Mars Reconnaissance Orbiter
NASA/JPL-Caltech/Univ. of Arizona

## Slide 8
Heat shield separation captured
by Curiosity’s Mars Descent Imager
NASA/JPL-Caltech/MSSS

## Slide 9
Kicking up dust just prior to landing
NASA/JPL-Caltech/MSSS

## Slide 10
“Touchdown confirmed.”
“Let’s see where Curiosity will take us.”
NASA/JPL-Caltech

## Slide 11
Curiosity self- portrait with navigation cameras
NASA/JPL-Caltech

## Slide 12
Navigation camera image showing the surface scour marks and rocks on the rover’s deck
NASA/JPL-Caltech

## Slide 13
Bedrock exposed by the landing engines in the scour mark named Goulburn
NASA/JPL-Caltech/MSSS

## Slide 14
ChemCam’s Remote Micro-Imager acquires high-res images of the Goulburn scour
Each image is 10-12 cm (4-5”) across
NASA/JPL-Caltech/LANL/CNES/IRAP/MSSS

## Slide 15
Curiosity and its tracks captured by
HiRISE on the Mars Reconnaissance Orbiter
NASA/JPL-Caltech/Univ. of Arizona

## Slide 16
Mastcam-34 mosaic of Mount Sharp, descent rocket scours, and rover shadow
NASA/JPL-Caltech/MSSS

## Slide 17
Mastcam-100 image of Mount Sharp’s layers, canyons and buttes
NASA/JPL-Caltech/MSSS
This boulder is the size of Curiosity

## Slide 18
Curiosity self-portrait using the arm-mounted Mars Hand-Lens Imager, through dust cover
NASA/JPL-Caltech/MSSS

## Slide 19
Curiosity images its undercarriage
with its Mars Hand-Lens Imager
NASA/JPL-Caltech/MSSS

## Slide 20
NASA/JPL-Caltech/LANL/CNES/IRAP/MSSS
ChemCam spectra of Coronation
NASA/JPL-Caltech/LANL/CNES/IRAP
NASA/JPL-Caltech/MSSS
Target: Coronation (N165)
Sol 13
Shots: 30
NASA/JPL-Caltech/LANL/CNES/IRAP/MSSS

## Slide 21
ChemCam’s laser induced breakdown spectrometer acquires a 5-spot raster
NASA/JPL-Caltech/LANL/CNES/IRAP/LPGN/CNRS
Before
After
Target: Beechey (Sol 19)
Power: 1 Gigawatt
Shots per spot: 50
8 cm(3”)

## Slide 22
Navigation camera mosaic of Curiosity’s robotic arm
NASA/JPL-Caltech

## Slide 23
Images of Curiosity’s turret centered
on MAHLI (left) and APXS (right)
NASA/JPL-Caltech/MSSS

## Slide 24
Nested, hand-lens imaging of the 25-cm (10”) high rock Jake Matijevic
NASA/JPL-Caltech/MSSS

## Slide 25
Curiosity’s Radiation Assessment Detector operated throughout the cruise to Mars
Particle Flux (protons/cm2/s/sr)
05
09
11
13
15
Day (March 2012)
Particle Flux (protons/cm2/s/sr)
RAD observed galactic cosmic rays and five solar energetic particle events
RAD was shielded by the spacecraft structure, reducing the observed particle flux relative to NASA’s ACE satellite
RAD is now collecting the first measurements of the radiation environment on the surface of another planet
NASA/JPL-Caltech/SwRI

## Slide 26
Curiosity’s Rover Environmental Monitoring Station is taking weather readings 24 × 7
REMS’ ground and air temperature sensors are located on small booms on the rover’s mast
The ground temperature changes by 90°C (170 degrees Fahrenheit) between day and night
The air is warmer than the ground at night, and cooler during the morning, before it is heated by the ground
NASA/JPL-Caltech/CAB(CSIC-INTA)

## Slide 27
Curiosity’s Rover Environmental Monitoring Station is taking weather readings 24 × 7
REMS’ pressure sensor is located inside the rover’s body
Each day the pressure varies by over 10%, similar to the change in pressure between Los Angeles and Denver
Solar heating of the ground drives an atmospheric “tidal wave” that sweeps across the planet each day
NASA/JPL-Caltech/CAB(CSIC-INTA)
Earth’s atmosphere = 101,325 Pascals, or about 140 times the pressure at Gale Crater

## Slide 28
Curiosity’s Dynamic Albedo of Neutrons experiment sounds the ground for hydrogen
DAN sends ten million neutrons into the ground, ten times a second
The “echo” back is recorded. If hydrogen is present in the ground, perhaps in aqueous minerals, some neutrons will collide and lose energy
NASA/JPL-Caltech/Russian Space Research Institute
DAN is used to survey the upper one meter of the ground below the rover as it drives along

## Slide 29
Curiosity is progressing toward Glenelg, where three distinct terrain types meet
NASA/JPL-Caltech/Univ. of Arizona

## Slide 30
Map view of conglomerate outcrops (next slides)
NASA/JPL-Caltech/Univ. of Arizona

## Slide 31
The Goulburn scour revealed the first look at underlying bedrock
NASA/JPL-Caltech/MSSS

## Slide 32
The conglomerate “Link” with associated loose, rounded pebbles
NASA/JPL-Caltech/MSSS

## Slide 33
“Hottah” reveals additional conglomerate, evidence of an ancient streambed
NASA/JPL-Caltech/MSSS

## Slide 34
Curiosity’s ultimate goal is to explore the lower reaches of the 5-km high Mount Sharp
NASA/JPL-Caltech/Univ. of Arizona